## Slide 1: Conducting a QRRA
Guidance for the Quality Department on facilitating Quality Requirements Risk Assessments
SLP 2.3.2.7_02 | SLF 2.3.2.7_02
Notes: Welcome. This session is for colleagues across the Quality Department. It covers how a Quality Requirements Risk Assessment (QRRA) is conducted under SLP 2.3.2.7_02, and, most importantly, the role we play in it. The key message: the QRRA is led and initiated by the Demander - the person accountable for specifying and buying the item. Quality facilitates and acts as the intelligent client.

## Slide 2
Why we are here
1
Ownership
Understand who leads the QRRA and where it fits in specification and procurement
2
Facilitation
Know how to support a QRRA session as the intelligent client, not the author
3
Consistency
Apply SLF 2.3.2.7_02 the same way every time: risk, Quality Grade, requirements, sign-off
What has changed
SLP 1.02.45 is now SLP 2.3.2.7_02 (Issue 1, effective 04/2026)
SLF 1.02.45.01 is now SLF 2.3.2.7_02 - the QRRA form
Content has transferred across; the process is unchanged in intent.
Watch out: SLP 4.06.08 (Issue 14) and older specifications still cite SLP 1.02.45. Read these as SLP 2.3.2.7_02.
Notes: Three objectives for today. Also flag the document change: SLP 1.02.45 has been superseded by SLP 2.3.2.7_02 and the form SLF 1.02.45.01 by SLF 2.3.2.7_02. The amendment record confirms content was transferred from SLP 1.02.45. Some documents, including SLP 4.06.08 Issue 14, still reference the old number - when you see it, point people to SLP 2.3.2.7_02 and the current form.

## Slide 3: Who owns the QRRA?
The Demander leads. Quality facilitates.
01
Notes: First, ownership. This is the point most often misunderstood.

## Slide 4
Roles in a QRRA
LEADS
Demander
Accountable for specification and procurement, e.g. Project Manager, Design Manager, PEM, Responsible Engineer or Demand Specifier. Initiates the QRRA, owns the risk assessment and records it on SLF 2.3.2.7_02.
NEEDS
Requestor
The person wanting the goods or services. Checks for a material master, specification and quality requirements, then launches procurement once they are in place.
FACILITATES
Quality (QM / QE)
The intelligent client. Advises on Quality Grade, risk and documentation; challenges and endorses. Accountable for applying oversight post award (step 1.6).
CONTRIBUTE
Key stakeholders
ICG, Construction, Commissioning Start-up / Operations, Engineering & Maintenance, SMEs and, where appropriate, the supply chain.
“It is essential that the Demander work collaboratively with key stakeholders” SLP 2.3.2.7_02, Purpose and Scope
Notes: SLP 2.3.2.7_02 defines the Demander as the accountable person responsible for product specification and procurement. SLP 4.06.08 says the same of the Demand Specifier: they ensure the risk assessment to assign the Quality Grade has been correctly carried out. So the QRRA belongs to them. The SLP also says the Demander must ensure the required oversight and assurance activities are captured on the QRRA. Quality is one of the key stakeholders, with a specific role: advise, challenge, endorse, and after contract award the QE is accountable for making sure the oversight is applied.

## Slide 5
Quality as the intelligent client
Facilitate, challenge, endorse
We bring the questions, the standards and the experience.
The Demander brings the requirement and owns the answer.
We do
Prompt with the Appendix 1 questions
Challenge component granularity and consequence ratings
Ask for a clear reason for each activity and LTR
Advise on Quality Grade, CQRs and ICG involvement
Share supplier, CFSI and lessons-learned insight
Endorse the agreed QRRA as part of the review team
We don’t
Write the QRRA on the Demander’s behalf
Set the Quality Grade in isolation
Apply one grade generically to a whole system
Accept “same as last time” without review
Add blanket inspection or LTRs with no rationale
Take over the procurement decision
Notes: This is what 'intelligent client' means in practice. We know enough about the requirement, the standards and the supply chain to ask the right questions and spot gaps, but we do not do the work for the Demander. If Quality writes the QRRA, ownership moves to the wrong place, the Demander's knowledge of how the item is used is lost, and the assessment becomes generic. The SLP is explicit that there should be a clear reason for each activity and that blanket gathering of records should be avoided.

## Slide 6: Where the QRRA fits
Triggers, process steps and the link to procurement
02
Notes: Next, where the QRRA sits in the wider process.

## Slide 7
SLP 2.3.2.7_02 at a glance
1.1
Understand what is needed and how it is used
Demander
1.2
Develop the specification
Demander
1.3
Identify and endorse quality requirements (QRRA)
Demander
1.4
Create a material master (if new)
Requestor
1.5
Launch procurement
Requestor
1.6
Apply quality oversight and assurance
Quality
1.7
Feed back on quality assurance and oversight
Quality
Where Quality comes in
Steps 1.1 to 1.3
Key stakeholder: advise and challenge as requirements are defined
Step 1.3
Integrated review team: endorse the QRRA and Quality Grade (and approve any QG 02P)
Steps 1.6 to 1.7
Accountable: oversight applied, CFSI and off-condition feedback
Notes: The flowchart on page 1 of SLP 2.3.2.7_02 has three swim lanes: Demander, Quality Manager (or nominated QE) and Requestor. The QRRA is produced at step 1.3, in the Demander's lane. Quality's own lane only starts at step 1.6 once procurement is launched. Before that we contribute as a key stakeholder and, at 1.3, as part of the integrated review team that endorses the final Quality Grade. Note the loop back to 1.3 if a CFSI issue is identified at step 1.6.

## Slide 8
When is a QRRA needed?
New plant and equipment
Triggered once safety and operational performance requirements are identified in the Product Verification Plan (SEMS 2.3.2.7)
Verification activities for the supplier are taken from the PVP and set out as quality requirements
Existing assets, goods and services
Triggered by replacement: obsolete or faulty equipment, or any service requested from a supplier
Evidence level comes from regulatory needs and Maintenance Schedules (SEMS 2.6.5.1)
Applies to everything
COTS, MOTS and bespoke items all complete step 1.3
Previous supplier performance is no guarantee of future performance
Review existing specifications and material masters: nothing should be assumed unchanged
Exemptions and simplifications
QG 04 items bought from the electronic catalogue are exempt. Where only minimal oversight is needed (e.g. a calibration certificate) it can be recorded on the material master or purchase requisition.
Notes: Triggers are in section 1.1 and 1.3 of the SLP. Stress that all items go through step 1.3, including COTS. Even repeat buys should be re-checked: SLP 2.3.2.7_02 says previous supplier performance is no guarantee and that where the Demander queries existing requirements they should contact Quality. The only exemption is QG 04 e-catalogue purchases. Technology-specific QRRA recommendations may also exist as addenda to Engineering Standards.

## Slide 9
How the QRRA links to procurement (SLP 4.06.08)
1.1
Make vs Buy analysis
SLP 4.06.24
1.2
Specify the requirement and agree Quality Grade
SLP 1.02.44 and SLP 2.3.2.7_02
1.3
Review requirements to select route
Frameworks, e-catalogue
1.4
Raise Purchase Requisition
Needs specification and Quality Grade
1.8
Procurement operations
Supply Chain Directorate
Trained Demand Specifiers only
The SAP Demander will not process a request from someone not on the trained Demand Specifier list
No Purchase Cards for QG 01 to 03
Purchase Cards must not be used for Quality Grade 01, 02 or 03 supplies or services
QG 01 and 02 go to ICG
The Supply Chain representative emails the Purchase Order and documents to ICG
Check the QASL first
No supplier without a grading on the Quality Assessed Supplier List (SLP 4.06.04)
Notes: SLP 4.06.08 step 1.2 requires the Demand Specifier to specify the requirement and agree the Quality Grade, considering risk and mitigation in line with SLP 1.02.45 - now SLP 2.3.2.7_02. The Demand Specifier must also make sure the appropriate risk assessment is conducted to define the correct Quality Grade. The Quality Grade is a required input to the Purchase Requisition at step 1.4. Under SLP 2.3.2.7_02 step 1.5, procurement can only commence once the specification, QRRA and lifetime records requirements are defined.

## Slide 10: Running a QRRA
Before, during and after the session
03
Notes: Now the practical part: how a QRRA session runs.

## Slide 11
Before the session
LEADS
Demander prepares
Defines the scope and how it will be broken down
Brings the specification (SEMS 2.3.2.6 / SLP 1.02.44) or COTS datasheet with OEM part numbers
Brings the PVP (SEMS 2.3.2.7) or Maintenance Schedule (SEMS 2.6.5.1)
Gathers existing material masters and previous QRRAs
Invites key stakeholders and books the session
FACILITATES
Quality gets ready
Reviews the pack in advance and notes questions
Selects relevant Appendix 1 prompts
Checks supplier history on the QASL and any CFSI or lessons learned
Identifies relevant standards and regulations (e.g. PUWER, LOLER, UKCA, BS EN 1090, BS EN 61508)
Confirms ICG availability where QG 01 or 02 is likely
Notes: The Demander arranges and prepares the session. If a Demander asks Quality to 'do the QRRA', redirect them: offer to facilitate, and help them prepare. Our preparation is about asking good questions: Appendix 1 of SLP 2.3.2.7_02 is our main tool. Regulated items (PUWER, LOLER, UKCA) and items built to standards with defined oversight (BS EN 1090 execution class, BS EN 61508 SIL) must be included on the QRRA.

## Slide 12
During the session: six steps through SLF 2.3.2.7_02
1
Break down the scope
Choose component granularity. Split Procurement / Fabrication from Site Installation. Include lifetime spares.
2
Assess consequences
Rate each item against the seven risk columns on the form.
3
Agree the Quality Grade
QG 01, 02, 02P, 03 or 04, driven by the consequences and the Appendix 2 ‘other factors’.
4
Select requirements
For each requirement, record who verifies it: SL, SL/MC, MC, Other or N/A.
5
Justify
Record the reason for each activity and the factors considered in Supporting Comments.
6
Confirm
Agree with all stakeholders and complete the ‘Confirmed by’ section.
The Demander leads every step. Quality prompts, challenges and checks the reasoning is recorded.
Notes: These six steps follow the structure of the form. Step 1: the SLP says oversight should relate to specific equipment or components, not be applied generically to a system, and the Demander, Designer or Requestor decides the granularity with the stakeholders. Steps 2 to 4 are covered on the next three slides. Step 5: the SLP requires a clear reason for each activity with the applicable consequences recorded. Step 6: sign-off.

## Slide 13
Step 2: rating the risk columns
Risk column | Rating | What to consider
Nuclear / Radiological Safety | SFC 1, SFC 2, SFC 3, SF, SM, SRE, NP, EE | Categorisation per SLSP 1.02.14.02; exposure or loss of containment
Conventional Safety | VH, H, M, L, N/A | COSHH, DSEAR, machinery, COMAH, LOLER, PUWER, pressure systems
Environmental | E1, E2, E3 | SLSP 1.02.14.02 s1.2, potential impact under fault conditions
Operational (TRAM) | VH, H, M, L, N/A | Throughput, reliability, availability, maintainability
Security | VH, H, M, L, N/A | Consequences of physical or cyber security failure
Grey Market | Is the OEM known? | CFSI exposure (SEMS 3.3.5.3, IAEA NP-T-3.26)
Business | VH, H, M, L, N/A | Cost, programme, commercial and reputational impact
Use Appendix 3 of SLP 2.3.2.7_02 for risk scoring criteria and consequences (Very High to Low).
Notes: Ratings and guidance are from the Guidance tab of SLF 2.3.2.7_02. The Demander should rate these, using the Responsible Engineer and SMEs for nuclear safety categorisation. Quality's job is to test the ratings: what happens if this component fails at point of use? Is it accessible? Can it be tested after installation? Appendix 3 gives criteria and consequences for each risk level.

## Slide 14
Step 3: agreeing the Quality Grade
Grade | Risk | Risk mitigation | Quality Plan
QG 01 | Very High | Inspection at supplier’s works by ICG | Required, approved before manufacture
QG 02 | High | Inspection at supplier’s works by ICG | Required, approved before manufacture
QG 02P | High (proprietary) | Manufacturer inspection; final inspection at Lillyhall Stores | Not required; justification on QRRA
QG 03 | Medium | Receipt inspection by ICG | By exception
QG 04 | Low / none | Transit damage and order completion check only | Not required
Minimum QG 03
Any item needing design, development or Sellafield Ltd inspection
QG 02P needs approval
Justification and risk assessment recorded on the QRRA, approved by Quality and the integrated review team
No agreement?
The Demand Specifier seeks advice from Quality and / or the relevant SME
Notes: From SLP 2.3.2.7_02 section 1.3 and Appendix 2. The grade sets which Contract Quality Requirements apply. Consider raising the grade if the item is complex, unique or novel, has a poor quality history, is inaccessible during operation, is hard to test after installation, or the potential economic loss is much larger than usual for that grade. The final grade is endorsed by the integrated review team, including the Requestor. Mandatory CQR deviations go through SEMS 3.3.6.2 to Supply Chain Quality.

## Slide 15
Step 4: selecting requirements and who verifies
Before manufacture
UKCA marking
Start-up meeting
Verification of contractor design
Approval of Quality Plan / ITP
People and procedures
Nuclear Safety Tool Box
Competent person qualifications
Weld, paint, NDT or test procedures
During manufacture
Material control
Interim inspection
Specialist testing (PT, LT, CT, LK, CFSI)
Acceptance test (FAT, SAT, CAT)
Release and records
Documentation (CofC, DofC, O&M, CC)
Final inspection
LTR review
Release certificate (5059 / 5199)
Packing and preservation
Verification codes: state who verifies each requirement
Yes (SL)
Sellafield Ltd
Yes (SL/MC)
SL and Main Contractor
Yes (MC)
Main Contractor
Yes (Other)
As specified
N/A
Not applicable
Notes: These are the requirement columns on SLF 2.3.2.7_02. The QRRA must identify which function delivers each element of assurance and oversight, e.g. Quality, ICG, Responsible Engineers, Construction or Commissioning. Extra requirements can be added as columns or in Supporting Comments. For large volumes, oversight can apply to first-off production and then revert to goods received inspection, defined in the ITP or Quality Plan. LTRs beyond those normally supplied with COTS go in the LTR schedule (SEMS 1.2.10.1).

## Slide 16
Questions to ask
From Appendix 1
Use open questions to test the Demander’s thinking.
Let them answer and record it; don’t answer for them.
Is it clear what oversight and LTRs the COTS product already includes?
Is it clear how these activities support the safety and security case?
Is the item complex, unique or novel?
Has the product or supplier had a poor-quality history?
Is the item accessible during normal operations?
Can functionality be proven after installation?
Is material traceability needed to achieve the performance condition?
Is in-process observation needed that final inspection can’t replace?
What witnessing of functional testing is needed for confidence?
Are the extra costs over the COTS standard understood and justified?
Notes: A selection of the Appendix 1 questions. Appendix 1 has general factors, factors from IAEA GS-G-3.5, specific factors to be read with SLP 1.10.315, and CFSI / grey market factors. Bring a copy to every session. These questions keep the Demander in the lead: they own the answers, we make sure the questions have been asked.

## Slide 17
CFSI and grey market: what to probe
Warning signs
Price lower than expected
Obsolete or hard-to-source items with short lead times
Chain of custody: is the item traceable to the OEM via authorised stockists?
Supplier is not the OEM, or is an independent distributor of unknown reputation
What to do
Record extra checks in the Specialist Testing column, with detail in the notes: functional testing, soak testing, enhanced visual and documentation checks
Reassess if an item once bought new is no longer available from an authorised source: repeat step 1.3 and update the material master
Prefer direct purchase from OEMs; see SEMS 3.3.5.3 for the CFSI process
Notes: CFSI is an area where Quality can add real value as intelligent client, because we see supplier performance and CFSI issues across the business. Use the CFSI / Grey Market factors in Appendix 1. A CFSI issue found during step 1.6 loops back to step 1.3 for a new risk assessment.

## Slide 18
Common pitfalls and good practice
Pitfall
Good practice
Quality writes the QRRA
Demander leads; Quality facilitates and endorses
One grade for the whole system
Grade at component level, including spares
Copying the last QRRA
Review existing requirements every time
Blanket LTRs and inspections
A clear reason for each activity and record
Supporting Comments left blank
Justify choices and reference Appendix 1 factors
Late stakeholder involvement
ICG, Construction, Commissioning in the room from the start
Notes: Common issues we see, each paired with what good looks like. Every good-practice point comes straight from SLP 2.3.2.7_02.

## Slide 19
After the session: sign-off and what comes next
Confirmed by
Delete or add roles as appropriate
Demander
Project Manager / PEM
Responsible Engineer / Designer
Project QE / Quality Manager
Construction Manager / Co-ordinator
ICG or Inspection Authority
Commissioning / Pre-operations
1
Check, approve and issue
Approve per SLP 1.02.42; issue to Project Document Control per SLP 4.09.108
2
Feed the specification
Append to the specification with the ITP and LTR schedule; reference on the PR and material master (SEMS 3.3.7.1); use for tender
3
Manage changes
Post-award: Contractor Request for Deviation (SEMS 3.3.6.2). Supplier changes: TQ, concession or production permit (SEMS 2.3.3.1)
4
Feed back
Off-condition, CFSI or lessons learned go to the Demander, RE and SMEs (step 1.7)
Notes: From the Guidance tab of SLF 2.3.2.7_02: once fully agreed by all stakeholders, the form is checked and approved per SLP 1.02.42 and issued to Project Document Control per SLP 4.09.108. The QRRA can be incorporated into the specification as an appendix, keeping the form format for consistency with ICG and the supply chain. Post award, the QE is accountable for making sure the oversight and LTR requirements are adhered to (SEMS 1.2.10.1 and SLP 1.10.315).

## Slide 20
Reference documents
Practices and forms | Title
SLP 2.3.2.7_02 | Determine quality oversight and assurance for procurement of plant and equipment (formerly SLP 1.02.45)
SLF 2.3.2.7_02 | Quality Requirements Risk Assessment form (formerly SLF 1.02.45.01)
SLP 4.06.08 | Procure works, supplies and services
SLP 1.02.44 | Prepare and publish a specification
SLP 4.06.04 | Quality Assessed Suppliers List (QASL)
SLP 4.06.24 | Make vs Buy analysis
SLP 1.10.315 | Deliver project quality assurance and control
SLSP 1.02.14.02 | Categorisation of nuclear safety, environmental and COMAH consequences
SEMS | Title
SEMS 2.3.2.7 | Product verification
SEMS 2.3.2.6 | Produce the design
SEMS 3.3.5.2 | Contract Quality Requirements Manual
SEMS 3.3.5.3 | Supplier sub-contractor procurement (CFSI)
SEMS 1.2.10.1 | Manage Quality (lifetime records)
SEMS 3.3.6.2 | Manage contract change and variations
SEMS 2.3.3.1 | Technical queries, concessions, production permits
SEMS 3.3.7.1 | Warehousing and inventory (material masters)
Notes: All referenced documents are on SEMS. Remember that SLP 1.02.45 and SLF 1.02.45.01 have been superseded by SLP 2.3.2.7_02 and SLF 2.3.2.7_02. SLP 1.02.42 (checking and approval) and SLP 4.09.108 (document control) apply at sign-off.

## Slide 21: Key takeaways
The Demander leads and owns the QRRA.
Quality facilitates, challenges and endorses as the intelligent client.
Every activity needs a clear, recorded reason.
Notes: Close by restating the three messages, then take questions. If colleagues are asked to 'do' a QRRA, the answer is: we will facilitate it with you.